## Slide 1: XI Computer Science UNIT-1
Chapter-3 Boolean Algebra
Introduction to Boolean Algebra
Logical Operators NOT, AND, OR, and Boolean Logic
Principle of Duality
Basic Postulates of Boolean Algebra
DeMorgan’s Theorem
Universal Gates (NAND, NOR) , XOR
Truth Tables
Logic Gates/Circuits

## Slide 2: What is Boolean algebra?
operation called NOT denoted by prime(’)/not/bar
symbol.
Boolean Algebra uses a set of Laws and Rules to define the operation of a digital logic circuit.
Who introduced it?
In 1854, Mathematician George Bool introduced a systematic treatment of logic and develop for this program and algebraic system called BOOLEAN ALGEBRA.
In 1938, Sennon demonstrated that the properties of by- stable switching circuits can be represented by this algebra and
called it SWITCHING ALGEBRA.
By what it is made oy???
A Switching Algebra or Boolean Algebra is an algebraic system consisting of the set {0,1} the binary operations ‘OR’ & ‘AND’ denoted the symbol ‘+’ and ‘.’ respectively and unary

## Slide 3: LOGICAL OPERATORS
Boolean algebra also deals with functions which have their values in the set {0, 1}. The basic operations of Boolean algebra are as follows:
Conjunction ( AND operation)
Disjunction ( OR operation)
Negation ( Not operation)
TRUTH TABLE:
A Truth Table is a table which represents all the possible input combinations of logical variables along with all the possible results/output of the given combinations of values.
LOGIC GATES:
Logic gates are the basic building blocks of any digital system. It is an
electronic circuit having one or more than one input and only one output. The relationship between the input and the output is based on a certain logic.
Based on this, logic gates are named as AND gate, OR gate, NOT gate etc.

## Slide 4: AnD Operator
Operation performed by AND operator is called
Logical Multiplication. Thus X.Y means X AND Y.
0.0=0
0.1=0
1.0=0
1.1=1
The Symbol and Truth table of AND gate
X Y | F= ( X.Y)
0 0 | 0
0 1 | 0
1 0 | 0
1 1 | 1
X Y
F

## Slide 5: OR Operator
X F Y | X Y | F=(X+Y)
 | 0 0 | 0
 | 0 1 | 1
 | 1 0 | 1
 | 1 1 | 1
Operation performed by OR operator is called
Logical Addition. Thus X+Y means X OR Y.
0+0=0
0+1=1
1+0=1
1+1=1
The Symbol and Truth table of OR gate

## Slide 6: nOT Operator
X | X’
0 | 1
1 | 0
This operator operates on single variable and operation performed by NOT operator is called
complementation. Thus X’ means complement of X.
0’=1
1’=0
The Symbol and Truth table of NOT gate
X X’

## Slide 7: What is Basic Postulates Of Boolean Algebra?
Boolean algebra, consists of fundamental laws that are used to build a workable, cohesive framework upon which are based the theorem of Boolean algebra. These fundamental laws are known as Basic Postulates Of Boolean Algebra.
POSTULATES | 
i. If X!=0 then X=1; If X!=1 then X=0 | ii. OR relations 0+0=0 0+1=1 1+0=1 1+1=1
iii. AND relations 0.0=0 0.1=0 1.0=0 1.1=1 | iv. NOT relations 0’=1 1’=0

## Slide 8: What is the Principle Oy Duality?
This principle states that starting with a Boolean relation, another Boolean relation can be derived by:
Changing each OR sign(+) to an AND sign(.)
Changing each AND sign(.) to an OR sign(+)
Replacing each 0 by 1 and each 1 by 0.
EXAMPLE:-
If X.Y=1 then its dual will be X+Y=0
, where X & Y belongs to 0,1.
EXAMPLE:-
If (X+Z)(Y+1)=1 then its dual will be X.Z+Y.0=0
, where X & Y belongs to 0,1.
NOTE:-
The derived relation using duality principle is called Dual Of Original Expression.

## Slide 10: 1.Properties of 0 and 1
a) 0+X=X
b) 1+X=1
c) 0.X=0
d) 1.X=X
0 X | R=X
0 0 | 0
0 1 | 1
1 X | R=1
1 0 | 1
1 1 | 1
0 X | R=0
0 0 | 0
0 1 | 0
1 X | R=X
1 0 | 0
1 1 | 1
0
X
X
1
X
1
0
X
0
1
X
X

## Slide 11: 2. Indempotence Law
a) X+X=X
X X | R=X
0 0 | 0
1 1 | 1
X X
X
b) X.X=X
X X | R=X
0 0 | 0
1 1 | 1
X
X
X
i.e., 0+0=0
1+1=1
i.e.,
0.0=0
1.1=1
The law states that,

## Slide 12: 3.Involution Law
(X’)’=X
X
X’
(X’)’=X
X | X’ | (X’)’ = X
0 | 1 | 0
1 | 0 | 1
The law states that,

## Slide 13: 4.Complementarity Law
a) X+X’=1
X X’ | R=X+X’
0 1 | 1
1 0 | 1
X
X’
b) X.X’=0
X X’ | R=X.X’
0 1 | 0
1 0 | 0
X.X’=0
i.e., 0+1=1
1+0=1
i.e.,
0.1=0
1.0=0
X+X’=1
X’
X
The law states that,

## Slide 14: 5.Commutative Law
X Y
R
Y X
R
a) X+Y=Y+X
The law states that,
X Y | R=X+Y | R=Y+X
0 0 | 0 | 0
0 1 | 1 | 1
1 0 | 1 | 1
1 1 | 1 | 1
+ is OR

## Slide 15: 5.Commutative Law
R
Y X
b) X.Y=Y.X
X Y | R=X.Y | R=Y.X
0 0 | 0 | 0
0 1 | 0 | 0
1 0 | 0 | 0
1 1 | 1 | 1
X Y
R
. is AND

## Slide 16: 6.Associative Law
a) X+(Y+Z)=(X+Y)+Z
Y Z
X
Y+Z
R
X
Y
R
Z
X+Y
X Y Z | Y+Z | X+Y | R=X+(Y+Z) | R=(X+Y)+Z
0 0 0 | 0 | 0 | 0 | 0
0 0 1 | 1 | 0 | 1 | 1
0 1 0 | 1 | 1 | 1 | 1
0 1 1 | 1 | 1 | 1 | 1
1 0 0 | 0 | 1 | 1 | 1
1 0 1 | 1 | 1 | 1 | 1
1 1 0 | 1 | 1 | 1 | 1
1 1 1 | 1 | 1 | 1 | 1
The law states that,

## Slide 17: 6.Associative Law
X Y Z | YZ | XY | R=X(YZ) | R=(XY) Z
0 0 0 | 0 | 0 | 0 | 0
0 0 1 | 0 | 0 | 0 | 0
0 1 0 | 0 | 0 | 0 | 0
0 1 1 | 1 | 0 | 0 | 0
1 0 0 | 0 | 0 | 0 | 0
1 0 1 | 0 | 0 | 0 | 0
1 1 0 | 0 | 1 | 0 | 0
1 1 1 | 1 | 1 | 1 | 1
Y
Z
Y
R
R
Z
X X
XY
YZ
b) X (Y.Z)=(X.Y) Z
The law states that,

## Slide 18: 7. Distributive Law (First)
Y
Z
R
X
Y+Z
Y
X
R
Z
XY
XZ
X Y Z | Y+Z | XY | XZ | R=X(Y+Z) | R=XY+XZ
0 0 0 | 0 | 0 | 0 | 0 | 0
0 0 1 | 1 | 0 | 0 | 0 | 0
0 1 0 | 1 | 0 | 0 | 0 | 0
0 1 1 | 1 | 0 | 0 | 0 | 0
1 0 0 | 0 | 0 | 0 | 0 | 0
1 0 1 | 1 | 0 | 1 | 1 | 1
1 1 0 | 1 | 1 | 0 | 1 | 1
1 1 1 | 1 | 1 | 1 | 1 | 1
a) X(Y+Z)=XY+XZ
The law states that,

## Slide 19: 7. Distributive Law (Second)
Y
Z
R
X
Y.Z
Y
X
R
Z
X+Y
X+Z
b)X+YZ=(X+Y).(X+Z)
R.H.S
= (X+Y).(X+Z)
=X.(X+Z)+Y.(X+Z)
= X.X+XZ+XY+YZ
=X+XZ+XY+YZ
=(X.1)+XZ+XY+YZ
=X(1+Z+Y) + YZ
=X.1+YZ
=X+YZ = L.H.S
Hence Proved
(Distributive Law1
X(Y+Z)=XY+XZ)
(Properties of 0 and 1)
(Properties of 0 and 1 , X=X.1)
(Properties of 0 and 1)
The law states that,
PROOF ( By Algebraic Method)

## Slide 20: 7. Distributive Law (Third)
X’Y
X’
Y
X
X
X Y
R
L.H.S.
= X+X’Y
=X.1+X’Y
=X(1+Y)+X’Y
=X+XY+X’Y
=X+Y(X+X’)
=X+Y.1
=X+Y
=R.H.S.
Hence Proved
PROOF ( By Algebraic Method)
(Complementarity Law) (Properties of 0 and 1)
(Properties of 0 and 1)
(Properties of 0 and 1)
c) X+X’Y=X+Y
The law states that,

## Slide 21: 8. Absorption Law
X
X
Y
a) X+XY=X
XY
X Y | X.Y | X+XY
0 0 | 0 | 0
0 1 | 0 | 0
1 0 | 0 | 1
1 1 | 1 | 1
=R.H.S.
PROOF ( By Algebraic Method)
L.H.S. = X+XY
=X(1+Y)
=X.1 = X
(By Properties of 0 and 1)
Hence Proved
The law states that,

## Slide 22: 8. Absorption Law
X
The law states that,
X
Y X.Y
PROOF ( By Algebraic Method)
b) X(X+Y)=X
L.H.S
=X(X+Y)
=X.X+X.Y
=X+X.Y
=X(1+Y)
=X
=R.H.S
Hence Proved
(Distributive Law ) (Indempotence Law)
(Properties of 0 and 1), 1+Y=1

## Slide 23: DeMorgan’s /irst Theorem
(X+Y)’=X’.Y’
X Y
R
X+Y
X’
Y’
X
Y
Let us assume that P=X+Y where P,X,Y are logical variables. Then, according to complementarity law,
P+P’=1 and P.P’=0.
i.e., if P=X+Y then P’=X’Y’ , so,
 | P+P’= | (X+Y)+X’Y’ | must be equal to 1
and | P.P’ = | (X+Y).(X’Y’) | must be equal to 0
It states that
NOTE: BOTH THE DEMORGANS THEOREM CAN BE PROVED USING TRUTH TABLE ALSO
X+Y
R
X’.Y’

## Slide 24: Let us prove the first part of 1st theorem, i.e., (X+Y)+(X’Y’)=1
Hence First Part Proved
(Distributive Law: A+BC=(A+B).(A+C) ) (Complementarity Law: X+X’=1)
(Properties of 0 and 1)
(Properties of 0 and 1)
L.H.S.
= (X+Y)+(X’Y’)
= (X+Y+X’).(X+Y+Y’)
= (1+Y).(X+1)
= 1.1
= 1

## Slide 25: Now, let us prove the second part of 1st theorem, i.e., (X+Y).(X’Y’)=0
Hence Second Part Proved
(Distributive Law): A+B).C=A.C+A.B (Associative Law): X.Y=Y.X (Complementarity Law): X.X’=0
(Properties of 0 and 1)
(Properties of 0 and 1)
L.H.S.
= (X+Y).(X’Y’)
= (XX’Y’)+(YX’Y’)
= (XX’Y’)+(X’YY’)
= (0.Y’) + (X’.0)
= 0+0
= 0
Thus, De-Morgan’s 1st Law proved
(X+Y)’=X’.Y’

## Slide 26: DeMorgan’s Second Theorem
(X.Y)’=X’+Y’
X
Y
R
XY
R
X’
Y’
X
Y
Let us assume that P=X.Y where P,X,Y are logical variables. Then, according to complementarity law,
P.P’=1 and P.P’=0.
i.e., if P=X.Y then P’=X’+Y’ so, we have to prove
P+P’= XY+(X’+Y’) must be equal to 1 and P.P’= XY.(X’+Y’) must be equal to 0
It states that,
XY
X’+Y’

## Slide 27: Let us prove the first part of 2nd theorem, i.e., XY+(X’+Y’)=1
L.H.S.
= XY+(X’+Y’)
=(X+X’+Y’).(Y+X’+Y’)
= (X+X’+Y’).(X’+Y+Y’)
= (1+Y’). (X’+1)
= 1.1
= 1
(Distributive Law: A+BC=(A+B).(A+C) )
(Commutative Law): X+Y=Y+X (Properties of 0 and 1): X+1=1
(Properties of 0 and 1): 1.1=1
Hence First Part Proved

## Slide 28: Now, let us prove the second part of 2nd theorem, i.e., XY.(X’+Y’)=0
L.H.S.
= (XY).(X’+Y’)
= XY.X’+XY.Y’
= X.X’.Y + X.Y.Y’
= 0.Y + X.0
= 0+0
= 0
Hence Second Part Proved
Thus, De-Morgan’s 2nd Law proved
(XY)’=X’+Y’
(Distributive Law): A+B).C=A.C+A.B (Associative Law): X.Y=Y.X (Complementarity Law): X.X’=0
(Properties of 0 and 1)
(Properties of 0 and 1)

## Slide 29
Boolean Algebra Rules |  | 
1. | 0+X=X | Properties of 0
2. | 0.X=0 | 
3. | 1+X=1 | Properties of 1
4. | 1.X=X | 
5. | X+X=X | Indempotence Law
6. | X.X=X | 
7. | (X’)’=X | Involution Law
8. | X+X’=1 | Complementarity Law
9. | X.X’=0 | 

## Slide 30
Boolean Algebra Rules |  | 
10. | X+Y=Y+X | Commutative Law
11. | X.Y=Y.X | 
12. | X+(Y+Z)=(X+Y)+Z | Associative Law
13. | (X.Y).Z=X.(Y.Z) | 
14. | X(Y+Z)=XY+XZ | Distributive Law
15. | X+YZ=(X+Y).(X+Z) | 
16. | X+XY=X | Absorption Law
17. | X(X+Y)=X | 
18. | X+X’Y=X+Y | Third Distributive Law
19. | (X+Y)’=X’.Y’ | Demorgan’s Theorem
20. | (X.Y)’=X’+Y’ | 

## Slide 32: NAND Gate
NAND gate is a universal gate which is a
combination of AND with NOT
input NAND Gate
X
Y
input NAND Gate
P Q R
input NAND Gate
A B C D
X | Y | X.Y | F= X.Y
0 | 0 | 0 | 1
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
X Y
F= X.Y
X | Y | Z | X.Y.Z | X.Y.Z
0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 0

## Slide 33: NOR Gate
NOR gate is a universal gate which is a combination of OR with NOT
2 input NOR Gate
X
Y
3 input NOR Gate
P Q R
4 input NOR Gate
A B C D
X | Y | X+Y | F=X+Y
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
X Y
F= X+Y
X | Y | Z | X+Y+Z | F=X+Y+Z
0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 0
F
F
F

## Slide 34: XOR Gate
XOR gate produces output 1 for only those input combinations that have ODD number of 1’s
3 input XOR Gate
P Q R
4 input XOR Gate
A B C D
No. of 1’s Even/Odd | X | Y | X + Y
Even | 0 | 0 | 0
Odd | 0 | 1 | 1
Odd | 1 | 0 | 1
Even | 1 | 1 | 0
X
Y
F = X + Y
No. of 1’s | X | Y | Z | F = X + Y + Z
Even | 0 | 0 | 0 | 0
Odd | 0 | 0 | 1 | 1
Odd | 0 | 1 | 0 | 1
Even | 0 | 1 | 1 | 0
Odd | 1 | 0 | 0 | 1
Even | 1 | 0 | 1 | 0
Even | 1 | 1 | 0 | 0
Odd | 1 | 1 | 1 | 1
F
F
XOR Addition can be summarized as:
0 + 0=0
1 + 0=1
0 + 1=1
1 + 1=0

## Slide 36: Q) Verify the following expression using Truth Table:
(A’+B’).(A+B) = A’.B + A.B’
Solution :
A | B | A’ | B’ | A’+B’ | A+B | (A’+B’).(A+B) | A’.B | A.B’ | (A’.B)+(A.B’)
0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 1
1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
Since, Column no. 7 and 10 are having same values as per the given
question. Hence, proved.

## Slide 38: Q) Draw a logic circuit for the following expression: F(x,y,z) = (x+y’+z).(x+y’+z’)
Solution:
X Y’ Z
X Y’
Z’
F
(X+Y’+Z).(X+Y’+Z’)
X+Y’+Z
X+Y’+Z’

## Slide 39
Q) Write the equivalent Boolean expression for the following logic circuit:
Solution :
F(A,B,C) = A’B+AB+B’C
F

## Slide 40: F(a,b,c) = (ab’c)+(c’b) Using NAND-to-NAND Logic Gate only.
Q) Draw a logic circuit for the following expression:
Solution:
A B C
C B
C’
B’
F(a,b,c)
(AB’C). (C’B)
= (AB’C)+ (C’B)
= (AB’C)+(C’B)
(A.B’.C)
(C’.B)
De-Morgan’s Theorem (applied).
NOTE: No need to solve. Directly write the answer. This is done just to prove and show.

## Slide 41: REFERENCES
Wikipedia
Tutorialspoint
XII Computer Science by Sumita Arora, Edition:2016

## Slide 42
Stay safe. Stay aware. Stay healthy. Stay alert.